HEXANE, HEXANES

Material Safety Data Sheet 
							  Identity (Trade Name As Used On Label)

| Manufacturer ES Industries | MSDS Number* 110-54-3 |
| --- | --- |
| Street Address 701 S Route 73 | CAS Number* 110-54-3 |
| City State Zip Code West Berlin, NJ 08091 | Date Prepared 09/01/05 |
| Phone Number 1-800-356-6140 (856) 753-8400 | Prepared By* Matthew Przybyciel |
| Fax Number (856) 753-8484 |  |

Section 1 – Material Identification and Information

| Components – Chemical Name & Common Names (Hazardous Components 1% or greater; Carcinogens 0.1% or greater) | OSHA PEL | ACGIH TLV | OTHER LIMITS RECOMMENDED |
| --- | --- | --- | --- |
| Aliphatic Hydrocarbons, C6H14, Hexane Hexyl Hydride | 500ppm | 500ppm | None |
| Non-Hazardous to ship |  |  |  |

Section 2 – Physical / Chemical Characteristics

| Boiling Point | 65ºC | Specific Gravity (H2O = 1) | @20ºC : 0.66 |
| --- | --- | --- | --- |
| Vapor Pressure (mm Hg and Temperature) | 125 @ 20ºC | Melting Point | Not Available |
| Vapor Density (Air = 1) | 3 | Evaporation Rate | Not Available |
| Solubility in Water | Insoluble | Water Reactive | No |
| Appearance and Odor | Clear, colorless liquid with gasoline like odor |

Section 3 – Fire and Explosion Hazard Data

| Flash Point and Method Used | -7ºF (tee) | Auto-Ignition Temperature | 225ºC | Flammability Limits in Air % by Volume | LEL 1.2% | UEL 7.5% |
| --- | --- | --- | --- | --- | --- | --- |

| Extinguisher Media | CO2 Dry chemical or foam |
| --- | --- |
| Special Fire Fighting Procedures | Self-contained breathing apparatus may be required |
| Unusual Fire and Explosion Hazards | Confined material can explode upon heating |

Section 4 – Reactivity Hazard Data

| STABILITY X Stable ⁪ Unstable | Conditions To Avoid | Vapor contact with spark, flame, a hot surface |
| --- | --- | --- |
| Incompatibility (Materials to Avoid) | Strong oxidizing agents |
| Hazardous Decomposition Products | Carbon monoxide |
| Hazardous Polymerization ⁪ May Occur X Will Not Occur | Conditions To Avoid | N/A |

Section 5 – Health Hazard Data

| PRIMARY ROUTES X Inhalation X Ingestion OF ENTRY X Skin Absorption ⁪ Not Hazardous | CARCINOGEN ⁪ NTP ⁪ OSHA LISTED IN ⁪ IARC Monograph X Not Listed |
| --- | --- |
| HEATH HAZARDS | Acute | If inhaled may be irritating to mucous membrane and upper respiratory |
|  | Chronic | Possible dermatitis from skin contact |
| Signs and Symptoms of Exposure | Can produce peripheral polyreurotherapy, eye irritation, nasal & respiratory passages, dizziness, nausea, unconsciousness, & dermatitis |
| Medical Conditions Generally Aggravated by Exposure |  |
| Emergency First Aid Procedures | Seek medical assistance for further treatment, observation and support |
| Eye Contact | Flush with large amounts of water, get medical attention |
| Skin Contact | Wash with soap and water |
| Inhalation | Remove to fresh air; give oxygen and artificial respiration if necessary |
| Ingestion | Do not induce vomiting, have victim drink 8 to 10oz of water to dilute |

Section 6 – Control and Protective Measures

| Respiratory Protection (Specify Type) | NIOSH – approved respirator should be worn in absence of adequate ventilation |
| --- | --- |
| Protective Gloves | Recommended | Eye Protection | Safety glasses |
| VENTILATION TO BE USED | X Local Exhaust | X Mechanical (general) | ⁪ Special |
|  | ⁪ Other (specify) |
| Other Protective Clothing and Equipment | Face shield, chemical resistant apron |
| Hygienic Work Practices |  |

Section 7 – Precautions for Safe Handing & Use / Leak Procedures

| Steps to be Taken if Material is Spilled or Released | Eliminate all ignition sources, wipe up or absorb excess and flush with water. |
| --- | --- |
| Waste Disposal Methods | To be performed in compliance with all current local, state, and federal regulations. |
| Precautions to be Taken in Handling and Storage | Use caution when handling or cleaning empty drums “empty” containers may retain dangerous product residue; keep containers closed when not in use. Do not handle near heat, sparks, flame or strong oxidizers. |
| Other Precautions and/or Special Hazards | Peripheral polyneuropathy is a progressive disorder of the nervous system which may become irreversible following sufficiently high exposure, this disorder has been observed in individuals exposed repeatedly to high vapor concentrations (1000-1500 ppm) of Hexane over a period of several months. |