METHYL ALCOHOL

Material Safety Data Sheet 
							  Identity (Trade Name As Used On Label)

| Manufacturer ES Industries | MSDS Number* 67-56-1 |
| --- | --- |
| Street Address 701 S Route 73 | CAS Number* 67-56-1 |
| City State Zip Code West Berlin, NJ 08091 | Date Prepared 09/01/05 |
| Phone Number 1-800-356-6140 (856) 753-8400 | Prepared By* Matthew Przybyciel |
| Fax Number (856) 753-8484 |  |

Section 1 – Material Identification and Information

| Components – Chemical Name & Common Names (Hazardous Components 1% or greater; Carcinogens 0.1% or greater) | OSHA PEL | ACGIH TLV | OTHER LIMITS RECOMMENDED |
| --- | --- | --- | --- |
| Methyl Alcohol- Methanol (Wood Alcohol) Hydroxyl Alphatic CH3OH, Carbinol, Wood Naptha, Monohydroxy Methane | 200ppm | 200ppm | N/A |
| Non-Hazardous to ship |  |  |  |

Section 2 – Physical / Chemical Characteristics

| Boiling Point | 64.5ºC (760mm) | Specific Gravity (H2O = 1) | 0.8 |
| --- | --- | --- | --- |
| Vapor Pressure (mm Hg and Temperature) | 97 @ 20ºC | Melting Point | -98ºC |
| Vapor Density (Air = 1) | 1.1 | Evaporation Rate | 5.9 |
| Solubility in Water | Miscible | Water Reactive | No |
| Appearance and Odor | Clear, colorless liquid with characteristic alcohol odor |

Section 3 – Fire and Explosion Hazard Data

| Flash Point and Method Used | 12ºC (tee) | Auto-Ignition Temperature | N/A | Flammability Limits in Air % by Volume | LEL 6.7% | UEL 38.5% |
| --- | --- | --- | --- | --- | --- | --- |

| Extinguisher Media | CO2 Dry chemical, “Alcohol” foam, water mist |
| --- | --- |
| Special Fire Fighting Procedures | Wear self-contained breathing apparatus |
| Unusual Fire and Explosion Hazards | Closed containers may explode upon heating |

Section 4 – Reactivity Hazard Data

| STABILITY X Stable ⁪ Unstable | Conditions To Avoid | Heat, contact with ignition source |
| --- | --- | --- |
| Incompatibility (Materials to Avoid) | Oxidizers, reactive metals, acids, acid chlorides, reducing agents |
| Hazardous Decomposition Products | Formaldehyde, carbon monoxide, nitrogen oxides |
| Hazardous Polymerization ⁪ May Occur X Will Not Occur | Conditions To Avoid | N/A |

Section 5 – Health Hazard Data

| PRIMARY ROUTES X Inhalation X Ingestion OF ENTRY X Skin Absorption ⁪ Not Hazardous | CARCINOGEN ⁪ NTP ⁪ OSHA LISTED IN ⁪ IARC Monograph X Not Listed |
| --- | --- |
| HEATH HAZARDS | Acute | Ingestion can produce blindness; can be fatal |
|  | Chronic | Prolonged or repeated skin contact may cause irritation |
| Signs and Symptoms of Exposure | Toxic by ingestion and inhalation. Affects central nervous system, especially optic nerve. Causes dizziness, muscle weakness, narcosis and respiratory failure. |
| Medical Conditions Generally Aggravated by Exposure | N/A |
| Emergency First Aid Procedures | Seek medical assistance for further treatment, observation and support |
| Eye Contact | Immediately flush thoroughly with large amounts of water |
| Skin Contact | Wash thoroughly with soap and water |
| Inhalation | Remove to fresh air; give artificial respiration if breathing has stopped |
| Ingestion | Drink four 8oz glasses of water, milk or 4% sodium bicarbonate; induce vomiting |

Section 6 – Control and Protective Measures

| Respiratory Protection (Specify Type) | NIOSH – approved respirator should be worn in absence of adequate ventilation |
| --- | --- |
| Protective Gloves | Butyl rubber, viton or equivalent should be worn to prevent skin contact | Eye Protection | Safety glasses with a side shield should be worn at all times |
| VENTILATION TO BE USED | X Local Exhaust | X Mechanical (general) | ⁪ Special |
|  | ⁪ Other (specify) |
| Other Protective Clothing and Equipment | N/A |
| Hygienic Work Practices | Wash thoroughly after handling. Do not take internally, eye wash and safety equipment should be readily available. |

Section 7 – Precautions for Safe Handing & Use / Leak Procedures

| Steps to be Taken if Material is Spilled or Released | Wipe up or absorb excess and flush with water; containerize for proper disposal. |
| --- | --- |
| Waste Disposal Methods | To be performed in compliance with all current local, state, and federal regulations. |
| Precautions to be Taken in Handling and Storage | Keep containers closed; Store in a cool area away from ignition sources and oxidizers. Do not breath vapor; do not get in eyes; avoid prolonged or repeated skin contact; do not take internally. |
| Other Precautions and/or Special Hazards | Electrically ground all equipment when handling this product. |